## Slide 1: Генерация идей
Notes: The WG has now collected all information regarding the chosen problem. Figures are controlled with energy and / or mass balance, and the WG starts the process of finding solutions to the problem. Sometimes possible improvements are quite obvious, others might be more difficult to find.
Our proposal is to try to see if there are more than one road to success. Perhaps the obvious one is not the best one. Therefore we strongly recommend you to try one of the given idea generating methods.
Hopefully, the WG will come up with ideas that are new and promising, and which will give your company the most effective and economic solution to the problem.
Normally, by looking at the proposals, you will find that some of them do not require any investments. These proposals we say belong to group A. Some other proposals may be obviously unrealistic at the time being. These we will put aside, but not forget. Times will change and possibly some of them can be relevant at a later time.
The rest of you ideas will have to be analysed and compared as for their benefit to the company.
As an example of the Brain Storming method, we use the example of the shower in a family of four persons.

## Slide 2
Notes: One picture with two faces. What do you see: An old woman with a big nose and mouth, or a young woman with her cheek and her necklass.

## Slide 3
Notes: The dripping tab.

## Slide 4: Текущий кран с горячей водой
Утечка: 0,01 (л/мин)
Утекает в год:
Q = 0,01 x 60 x 24 x 365/1000 = 5,25 (м3/год)
Энергия для нагрева воды: k = 1,16 (кВтч/м³/град.C)
Вода нагревается с 5 до 65 oC. T = 60 (град. C)
E = k x T x Q = 1,16 x 60 x 5,25 = 365 (кВтч/год)
Данные о стоимости:
Чистая вода: Wt = 18.94 руб/м³
Сточная вода: Ws = 15.07 руб/м³
Электричество: Ec = 4.01 руб/кВтч
Стоимость за год: C = E x Ec + (Wt + Ws) x Q
С = 1479.69+178.55 = 1658.2 руб.
Notes: The cost during one year when the leakage is hot water.

## Slide 5: Препятствия творчеству
Боязнь:
сделать ошибку
быть раскритикованным
изменений
нарушить традиции

## Slide 6: Четыре правила
Критиковать идеи строго запрещается
Расслабьтесь и забудьте все формальности
Нам надо как можно больше идей
Ищите возможности объединения идей и улучшений
Notes: We want to activate the subconsience and to forget the engineering training.

## Slide 7: Мозговой штурм
Выберите лидера группы.
Выберите секретаря для записи всех идей.
Согласитесь о правилах процедуры.
Сформулируйте проблему.
Помните о четырех правилах.
Завершите мозговой штурм через 30-40 минут.

## Slide 8: Чему уделить внимание
Сырьё:
Замена токсичных материалов на менее токсичные или нетоксичные
Совершенствование процесса отбора закупаемого сырья, обращения с сырьём и его хранения
Проведение обучения рабочих
Изменение оборудования:
Установка оборудования, производящего минимальное количество отходов и выбросов или не производящего их вовсе
Модернизация оборудования или производственных линий с целью минимизации выбросов и отходов
Повышение эффективности эксплуатации оборудования
Устранение источников протечек и утечек
Усовершенствование планов технического обслуживания оборудования
Notes: Having this on your mind will help you in the search of improvements.

## Slide 9: Чему уделить внимание
Изменения производственного процесса:
Оптимизация процесса и использования сырья
Изменение условий прохождения процессов или технологии производства для сокращения образования загрязнения и отходов
Организация контроля и проведение измерений
Проведение обучения рабочих
Переработка и повторное использование:
Внедрение замкнутых систем
Разделение потоков отходов и стоков
Переработка на предприятии
Переработка вне предприятия
Организация обмена отходами (отход как сырьё)

## Slide 10: Водоснабжение
Notes: Chematic presentation of a water system. Red arrow indicates hot water. Blue process need heating, red needs cooling, grey is dirty and green is cleen.

## Slide 11: Водоснабжение (альтернативный вариант)

## Slide 12: Цех окраски
Notes: A bath for painting of parts in a continous transport line. Paint is lost giving a cleaning problem.

## Slide 13: Цех окраски (улучшенная организация)
Notes: Transport line is stopped at intervals to allow paint to drip back into the container.